## Slide 1
RockOn! 2017
Accelerometer Calibration
Notes: Go to: Gyro, Pres_Temp

## Slide 2
Accelerometer Calibration
Objectives
  Determine calibration values for the accelerometer 3g, 16g, and 50g sensors
Notes: Go to: Gyro, Pres_Temp

## Slide 3
Accelerometer Calibration
Background
  Follow the same testing procedure you used earlier to calibrate your accelerometers. You can ignore the other sensor tests.
Notes: Go to: Gyro, Pres_Temp

## Slide 4
Accelerometer Calibration
Calibration
  When you have finished obtaining data, power off, remove the SD card and get data from SD by inserting into your laptop
Notes: Go to: Gyro, Pres_Temp

## Slide 5
Accelerometer Calibration
Calibration
  Select cell D2 and calculate C2*4.9 to get your mV readout by typing “ = C2 * 4.9” in the function box and hitting enter. Repeat this step for C3 also.
D3 “ = C3 * 4.9”
Notes: Go to: Gyro, Pres_Temp

## Slide 6
Accelerometer Calibration
Calibration
  Select D3 and D4 and double click the small square in the lower right hand corner of the selected cells
  Excel will now calculate the remaining rows as you did for D3 and D4
Notes: Go to: Gyro, Pres_Temp

## Slide 7
Accelerometer Calibration
Calibration
This is what your file should look like so far
Notes: Go to: Gyro, Pres_Temp

## Slide 8
Accelerometer Calibration
Calibration
  Repeat this for each axis of each accelerometer so that all your columns have been converted to mV
  Label each of these new columns with the same name as the column it was copied from (the name of the column just to the left)
Notes: Go to: Gyro, Pres_Temp

## Slide 9
Accelerometer Calibration
Calibration
  This is what your file should look like now:
Notes: Go to: Gyro, Pres_Temp

## Slide 10
Accelerometer Calibration
Calibration
  Hold down Ctrl and select the converted columns. Copy these columns and in the AccelCalibration Excel spreadsheet, select cell B1 and paste.
Notes: Go to: Gyro, Pres_Temp

## Slide 11
Accelerometer Calibration
Calibration
  This is what AccelCalibration should look like after you paste:
Notes: Go to: Gyro, Pres_Temp

## Slide 12
Accelerometer Calibration
Calibration
  Select both of the cells containing “1” and “2” in column A and click the small square in the lower right hand corner of the selected cells. This will provide indices for all your data.
Notes: Go to: Gyro, Pres_Temp

## Slide 13
Accelerometer Calibration
Calibration
  Hold down Ctrl and select columns A, B, C, and D
  Click “Scatter” and “Scatter with smooth lines”. Column A will automatically be the x axis of the plot
Notes: Go to: Gyro, Pres_Temp

## Slide 14
Accelerometer Calibration
The graph you just made should be similar to this one
You may want to change the y axis limits. Do this by double-clicking on the y axis numbers (boxed in the picture)

## Slide 15
Accelerometer Calibration
In the axis limits box, change the options minimum and maximum to fixed, and enter the range you want

## Slide 16
Accelerometer Calibration
This is the graph for the low range accelerometers
Notice that areas of +1g, 0g, and -1g are clearly visible on the graphs as flat areas
The Z accelerometer, on the other hand, reads about 70mV above the other two, the equivalent of more than 1g!
-1g
+1g
0g

## Slide 17
Accelerometer Calibration
- This is the graph for the medium range accelerometers
Notice that the X, Y, and Z accelerometers seem to have produced similar outputs.
On this particular graph, the three sensors produce very similar outputs, but on careful examination slight shifts are visible
  - To graph, Hold down Ctrl and select columns A, E, F, and G
  - Click “Scatter” and “Scatter with smooth lines”.

## Slide 18
Accelerometer Calibration
This is the graph for the high z accelerometer
This output is much more messy than the other sensors. This is because it is a high-range sensor
The number of bits per g is lower since there are more g’s to measure, so the resolution is lower also
  - To graph, Hold down Ctrl and select columns A and H

## Slide 19
Accelerometer Calibration
- Notice the list of values in column J. At the moment, they are just dummy values, so you need to fill them in. Read the actual values off the flattest parts of the graphs by moving your mouse over them.
Read value
from here
(Y Low, -1g)
And
put it
here

## Slide 20
NOTE: It is difficult to determine the 0g values on the Z-Axis. So, you have to look at the Z-Axis during the X-Axis or Y-Axis -1g and 1g data test points. Or, you can take the average of the highest and lowest Z-Axis data test points during the -1g and 1g test points.
Accelerometer Calibration
X-Axis -1g & 1g Data Test Points
Y-Axis -1g & 1g Data Test Points
Determine an approximate value
Take an Average of the maximum and minimum of the flat regions

## Slide 21
Accelerometer Calibration
The graphs and the corresponding equations will update automatically
*Note: It may be helpful to record the flat data points on a separate piece of paper to be copied into the Excel sheet.

## Slide 22
Accelerometer Calibration
Those equations can be used to convert from voltage to acceleration.
Copy column A into column AG to get the right number of indexes.
Then copy the equations from the top of each graph into the corresponding cell in row 2 of columns AH through AN by multiplying the cell by the equation. The “X” from the equation is then represented by the cell, for example, B2.
Notes: Note that your slope value should be less than 1. If you invert it, it gives you the mV/g value (~60 for low axis accels for example)

## Slide 23
Accelerometer Calibration
Select cell AH2. As before, double click the small square in the bottom right corner of the selected cell to fill the conversion down.
Repeat for the other accelerometers.

## Slide 24
Accelerometer Calibration
Graph the converted data. You should now see all flat areas at -1g, 0g, or 1g
Repeat for X, Y, and Z Med accelerometers and the Z High accelerometer
You will use these calibration conversions with your flight data

## Slide 25
RockOn! 2017
Gyroscope Calibration
Notes: Go to: Gyro, Pres_Temp

## Slide 26
Gyroscope Calibration
Background
  Next we will account for the offset in the gyro values. The gyro data should be centered around 0, otherwise it will indicate higher or lower spin rates that what was truly present during flight
Notes: Go to: Gyro, Pres_Temp

## Slide 27
Gyroscope Calibration
Go back to the parsed data and select the three gyro data columns
Notes: Go to: Gyro, Pres_Temp

## Slide 28
Gyroscope Calibration
  Copy this data and paste it into cell B1 in the GyroCalibration excel file
Notes: Go to: Gyro, Pres_Temp

## Slide 29
Gyroscope Calibration
Calibration
  Select both of the cells containing “1” and “2” in column A and click the small square in the lower right hand corner of the selected cells. This will provide indices for all your data.
Notes: Go to: Gyro, Pres_Temp

## Slide 30
Gyroscope Calibration
Calibration
  This output is already in o/s, but sometimes the baseline value is not centered around 0, as shown in the picture
Notes: Go to: Gyro, Pres_Temp

## Slide 31
Gyroscope Calibration
Calibration
  Plot one column of gyro data and look for a location where the rotation is “zero”. This will be a flat spot in the data when you were not moving your board
Good, steady
output
Notes: Go to: Gyro, Pres_Temp

## Slide 32
Gyroscope Calibration
Calibration
  Hover your mouse near the start of this section to determine which samples you need to start at for your average.
Notes: Go to: Gyro, Pres_Temp

## Slide 33
Gyroscope Calibration
Calibration
  Hover your mouse near the end of this section to determine which samples you need to stop at for your average.
Notes: Go to: Gyro, Pres_Temp

## Slide 34
Gyroscope Calibration
Calibration
  The previous picture showed that the steady range covers ~390 data points. Use the AVERAGE Function to average the data range for the gyro x data in K4
Notes: Go to: Gyro, Pres_Temp

## Slide 35
Gyroscope Calibration
Calibration
  Repeat this process for Gyro Y and Gyro Z
Notes: Go to: Gyro, Pres_Temp

## Slide 36
Gyroscope Calibration
Calibration
  Now we need to subtract this offset from each data column. If the offset is less than +/-1, it is not necessary to subtract it out.
  Copy your Sample column into column U
Notes: Go to: Gyro, Pres_Temp

## Slide 37
Gyroscope Calibration
Calibration
  In V2, subtract the Gyro X average in K4 from the first Gyro X data value in B2. Put a “$” in front of each index for the average value ($K$4). This will hold this box constant, instead of incrementing it when we extend this to the entire data column
Notes: Go to: Gyro, Pres_Temp

## Slide 38
Gyroscope Calibration
Select cell V2. As before, double click the small square in the bottom right corner of the selected cell to fill the conversion down.
Repeat for the other gyroscope data sets
=B2-$K$4
=C2-$K$5
=D2-$K$6

## Slide 39
Gyroscope Calibration
Now each data column should have data centered around 0
Record the average values on your checklist for use after flight

## Slide 40
RockOn! 2017
END
Calibration
Notes: Go to: Gyro, Pres_Temp